SI 633  Winter 2009

Technical terms, The Coming of the Book, chapter 2:

punch, die, intaglio, casting vs. die stamping, matrix/matrices, mold, a sort, a custom, linotype, monotype, galley, lead, forme, bed, platen, frisket, tympan:  HUH?

Three basic types of printing:

From below surface of paper (or other material to be printed upon):

intaglio :  Image cut or etched into a plate (usually metal, usually copper); plate then inked

and pressed to paper

From a flat plane:

lithograph : Image marked on a flat surface (stone [Grk lithos], metal) with some areas

treated with oil or fat to repel ink.  Developed in Germany around 1798 by Alois

Senefelder.

From raised type pieces:

 letterpress : Image formed by assemblage of many individual movable pieces

Four different types of press (in order of chronological development):

platen press:  paper is pressed by a flat surface onto a block of metal type (the “forme”)

cf. Gutenberg-era wine press technology

rubber press:  a rubber blade moves over the paper to press it against inked surface

cylinder press:  a cylinder presses the paper to the inked surface by rolling over the sheet

rotary press:  paper is pulled in a continuous roll through two cylinders touching each other

(cf. old movies containing scenes of newspapers being printed)

Creating type:

punch:  the beginning of creating a letter of type.  Hard metal engraved with the RAISED

form of a letter.  Requires painstaking detail work done by practiced metalsmith.

matrix: the INDENTED image of the letter formed by the punch striking this piece,

of necessity softer metal than that of the punch; the face of the type that will be

pressed to the paper.  Before having its edges trimmed and leveled, a matrix is called a

“strike.”  The trimming is called “justification.”   Also called the “die.”

slug:  a set of matrices lined up to create (“cast”) a line of type ready for use

sort:  the individual letter created

Important moments in technological advancement:

the printing press goes mechanical (no more turning of the parts by hand) by the application

of steam power to printing in the early 19th century; the rotary press is first used in

Germany in 1812

typesetting is automated (no more standing at a case and putting type into a composing stick		by hand) by the 1880s invention of the Linotype (pron. “line o’ type”) machine

(Germany)

typesetting goes digital by use of computers in the 1960s

Source:  G. A. Glaister, Encyclopedia of the Book, 1996